## Slide 1: Real World Tips, Tricks and Best Practices
St Louis SolidWorks User Group
January 21, 2026
Greg Kemner
Senior Mechanical Design Engineer
Schoellhorn-Albrecht Machine Co.
https://www.schoellhorn-albrecht.com/
St. Louis, MO
Contact: Greg Kemner | LinkedIn

## Slide 2: Overview
Drawing Performance Tips
  Save Model Data option
  Draft vs High Quality View Display
Improve Productivity
  Styles/Favorites in Drawings and Models
  Link Items to Notes in Drawings
  Dimension Angle to Imaginary Line
Assembly Tips
  Breadcrumbs
  Group Mates by STATUS in Feature Tree
Feature Tree Productivity Tips
  Naming Features, Searching Tree, Split Tree Display
  Favorites, Show/Hide, Model Display Style
Support and Training Options
Tech Support vs Application Engineer Comparison Example

## Slide 3: Drawing Performance – Save Model Data
“Save Model Data” – Introduced in SW 2020
Great idea in concept
Takes a snapshot of drawing views and stores that info in the file
You can then quickly open a large drawing to Detail it (dimension, notes, etc.) without taking the time to retrieve the underling CAD Model
Issues
  Only few people need or will utilize it
  Is turned “ON” by Default even though only few will need/use it
  DOUBLES file size on hard drive (due to saving the view snapshot information as part of the drawing file)
  DOUBLES retrieval time if you are fully retrieving the drawing and model
  INCREASES save time
  It is a DOCUMENT Property NOT a SYSTEM Option
    MUST set it for each and every individual drawing
My problem drawing file size went from 800 mb down to 410 mb.
Retrieval time over the network went from 10 minutes down to 5 minutes
Recommendations:
  Turn off in your drawing templates
  Check every drawing you open/work on and confirm it is OFF unless you specifically want it on
  Create a macro to automate setting

## Slide 4: Drawing Performance – Draft vs High Quality Drawing View Display Style
Bug with Shaded Views Display Style Display Quality - BR10000359698
  Switches to Draft Quality by default when you select Shaded View Display
  Issue started in SW 2022
  Resolved in SW 2026 SP0
High Quality View Display Style Benefits
  Reduces drawing retrieval time
  Reduces drawing update and regeneration time
  Reduces time switching between sheets
  Significantly reduces file size and data storage (by as much as 50%)
  Improves print image quality (on paper or in a pdf)
My problem drawing file size went from 410 mb down to 205 mb.
Retrieval time over the network went from 5 minutes down to 1 min 50 seconds.
Check all existing or newly created SHADED views you find in all drawings:
  New Drawing
  Old Drawing
  Copying a Drawing
  Revising a Drawing
  Adding New Shaded View
  Existing Shaded Views or Switching an Existing View to Shaded

## Slide 5: Improve Productivity
Manually Enter/Overridden data is your enemy
Use the Power of the Software
Work Smarter – Not Harder
What is something you do all the time?
  Time consuming
  Repetitive
  Tedious
  Complicated
What is something you only do occasionally?
  That you have to relearn every time you do it.
There is usually a better way

## Slide 6: Styles/Favorites
DRAWINGS
  Dimensions
  Balloons
  Surface Finish
  Weld Symbols
  Notes
  Geometric Tolerance
MODELS
  Dimensions
  Hole Wizard
  Advanced Hole
Set Default Folder:
  SYSTEM OPTIONS -> FILE LOCATIONS -> DIMENSION/ANNOTATION FAVORITES
***File Specific (Part/Drawing)***
  Load all Styles/Favorites into your template Part and Drawings so they are available in all new files you create.
  Load into existing Part and Drawings as needed.
Setup Styles/Favorites for:
  Things you do all the time
  Things you occasionally do but have to relearn every time you do them.
  Company Standards
Document
Default
Add or Update
Style
Delete
Style
Save to Folder
Open from Folder
Select the Style to use from the Drop-Down List
Known Bugs
Weld Symbol Style - BR10000418269
Note Style - BR10000418272
Geom Tol Style - BR10000418281

## Slide 7: Link Items to Notes
Dimensions, Balloons, Symbols, GD&T, etc.
  Simply click on an item as you enter text in your note and it will appear in your note.
  To change anything about the item display in the note you must go back to the original item and change it there.
  If you delete the original item, it remains displayed in your note, BUT will no longer update or be able to be changed
Custom Properties - Assembly, Sub-Assy, Part or Body/Cut-List Custom Properties
  Current Drawing View
  Selected component for other drawing view
    You must pick on your desired item in the drawing immediately after choosing this option
    ***Solidworks gives you NO indication to select something***
    You just must know to do that!
    Right click on the screen to “Select Other” if you want to select say a Sub-Assy model instead of a component part.
  Component to which the annotation is attached
Link to Property
Link Table Cell

## Slide 8: Dimension Angle to Imaginary Line
Pick the angled geometry
Select a vertex at one end of that angled geometry
Crosshairs will appear at the vertex you selected
Pick the direction of the crosshairs that you want to dimension to
It creates the desired angle dimension to an imaginary reference

## Slide 9: Assembly Tips
Breadcrumbs
  Allows quick access to mates and features
  Show at mouse pointer instead of at top of screen
  System Options -> Display -> Breadcrumbs
Group mates by STATUS in Model Tree

## Slide 10: Feature Tree - Productivity
In large models or assemblies, I find I spend a lot of time scrolling up and down the Feature Tree looking for specific features or components.
Name Key Features to make them easier to find
  Temporary Names
  Permanent Names
Search Feature Tree by Name (feature or component)
  Plane, Sketch, McMaster
  Filter Display based on Results

## Slide 11: Feature Tree – Productivity (cont.)
Split Tree Display
  Grab the Splitter Bar and Drag Down to Split Tree
  Show 2 Feature Trees
  Show Feature Tree + Configuration Tree

## Slide 12: Feature Tree – Productivity (cont.)
Favorites – Top of the Feature Tree
  Features or Components to the “Favorites” folder
  Right Click Feature or Component -> Add to Favorites
  Drag and Drop into Favorites Folder
  Does not Change Feature Tree Order
    Just adds a link in the Favorites Folder to the chosen Feature or Component for Quick Access.
Show/Hide
Set Display Type
  Check Mark indicates Default Display Type

## Slide 13: Support and Training
Utilize the resources available to you
Make the most out of the money you are spending for yearly maintenance
There are 3 main components
  Training – Learn New functionality or Skills
  Tech Support – Verify functionality is working properly, sometimes explain how functionality works/is intended/limitations
  Application Mentoring Sessions – Best Practices on applying functionality to your specific application or need
Elite Success Plan
  Includes Free Detailed/In Depth Self Paced Online Training Classes
    Can jump around between topics in each class to skip things you already know
    You WILL learn something new, even if it is something you have been doing a long time
  Application Mentoring Sessions
    1 hr Direct Sessions with an Application Engineer on a specific topic.
    Can be 1-on-1 or part of a group for a meeting
    Best practices and recommendations
    You get Qty 2 – 1-hour sessions per SolidWorks License per Year
      12 licenses = Qty 24 – 1-hour sessions per year

## Slide 14: Tech Support vs Application Engineer
Problem Background
  Complex casting with draft, rounds and chamfers someone else started that I was finishing
  Odd issues where rounds and chamfers would work fine in one location but fail in another identical location.
  Rounds with identical dimensions and properties would display properly in one location and look completely different in a different (but identical) location.
Tech Support
  Examined rounds and chamfers to see if there was a bug or functionality issue.
Application Engineer
  Looked at the model as a whole and identified that the 1st feature was a Loft
  Pointed out that Extrude and Revolve features are calculated very exactly and precisely.
  Features such as a Loft where there is blending and interpretation occurring between 2 or more sections is, by that very nature, a much less exact or precise feature.
  As a result, you can sometimes run into odd behavior with downstream features that are built upon it.
Conclusion/Results
  I rebuilt the model from the 1st feature, changing the Loft to an Extrude with Draft.
  Rerouted all the features along the way.
  Then ALL Rounds and Chamfers worked correctly and looked properly in all locations at the end!